## Slide 1: CSE 340 Computer Architecture Spring 2018 MIPS ISA Review

## Slide 2: How Do the Pieces Fit Together?
I/O system
Instr. Set Proc.
Compiler
Operating
System
Application
Digital Design
Circuit Design
Instruction Set
Architecture
Firmware
Coordination of many levels of abstraction
Under a rapidly changing set of forces
Design, measurement, and evaluation
Datapath & Control
Memory
system
Notes: For lecture

## Slide 3: Processor Organization
Control needs to
  input instructions from Memory
  issue signals to control the information flow between the Datapath components and to control what operations they perform
  control instruction sequencing
Fetch
Decode
Exec
CPU
Control
Datapath
Memory
Devices
Input
Output
Datapath needs to have the
  components – the functional units and storage (e.g., register file) needed to execute instructions
  interconnects - components connected so that the instructions can be accomplished and so that data can be loaded from and stored to Memory

## Slide 4: Below the Program
High-level language program (in C)
  swap (int v[], int k)
  (int temp;
  temp = v[k];
  v[k] = v[k+1];
  v[k+1] = temp;
  )
Assembly language program (for MIPS)
  swap: sll $2, $5, 2
  add $2, $4,$2
  lw $15, 0($2)
  lw $16, 4($2)
  sw $16, 0($2)
  sw $15, 4($2)
  jr $31
Machine (object) code (for MIPS)
  000000 00000 00101 0001000010000000
  000000 00100 00010 0001000000100000
    . . .
Notes: For class handout

## Slide 5: Below the Program
High-level language program (in C)
  swap (int v[], int k)
  (int temp;
  temp = v[k];
  v[k] = v[k+1];
  v[k+1] = temp;
  )
Assembly language program (for MIPS)
  swap: sll $2, $5, 2
  add $2, $4,$2
  lw $15, 0($2)
  lw $16, 4($2)
  sw $16, 0($2)
  sw $15, 4($2)
  jr $31
Machine (object) code (for MIPS)
  000000 00000 00101 0001000010000000
  000000 00100 00010 0001000000100000
    . . .
C compiler
assembler
Notes: For lecture
Computer only understands zeros and ones – instructions of 0’s and 1’s
Early programmers found representing machine instructions in a symbolic notation – assembly language
And developed programs that translate from assembler to machine code
Eventually, programmers found working even in assembler too tedious so migrated to higher-level languages and developed compilers that would translate from the higher-level languages to assembler

## Slide 6: RISC - Reduced Instruction Set Computer
RISC philosophy
  fixed instruction lengths
  load-store instruction sets
  limited addressing modes
  limited operations
MIPS, Sun SPARC, HP PA-RISC, IBM PowerPC, Intel (Compaq) Alpha, …
Instruction sets are measured by how well compilers use them as opposed to how well assembly language programmers use them
Design goals: speed, cost (design, fabrication, test, packaging), size, power consumption, reliability, memory space (embedded systems)
Notes: As opposed to CISC – Complicated Instruction Set Architecture (ala the x86)

## Slide 7: MIPS R3000 Instruction Set Architecture (ISA) Microprocessor without Interlocked Pipeline Stages
Instruction Categories
  Computational
  Load/Store
  Jump and Branch
  Floating Point
    coprocessor
  Memory Management
  Special
R0 - R31
PC
HI
LO
Registers
OP
OP
OP
rs
rt
rd
sa
funct
rs
rt
immediate
jump target
3 Instruction Formats: all 32 bits wide
R format
I format
J format

## Slide 8: Review: Unsigned Binary Representation
Hex | Binary | Decimal
0x00000000 | 0…0000 | 0
0x00000001 | 0…0001 | 1
0x00000002 | 0…0010 | 2
0x00000003 | 0…0011 | 3
0x00000004 | 0…0100 | 4
0x00000005 | 0…0101 | 5
0x00000006 | 0…0110 | 6
0x00000007 | 0…0111 | 7
0x00000008 | 0…1000 | 8
0x00000009 | 0…1001 | 9
 | … | 
0xFFFFFFFC | 1…1100 | 
0xFFFFFFFD | 1…1101 | 
0xFFFFFFFE | 1…1110 | 
0xFFFFFFFF | 1…1111 | 
232 - 1
232 - 2
232 - 3
232 - 4
232 - 1
1 1 1 . . . 1 1 1 1 bit
31 30 29 . . . 3 2 1 0 bit position
231 230 229 . . . 23 22 21 20 bit weight
1 0 0 0 . . . 0 0 0 0 - 1
Notes: All positive numbers - no sign bit
last entry is most significant byte address
fourth from last entry is most significant word address

## Slide 9: Review: Memory Organization
• Viewed as a large, single-dimension array, with an address.
• A memory address is an index into the array
• "Byte addressing" means that the index points to a byte of memory.
Notes: All positive numbers - no sign bit
last entry is most significant byte address
fourth from last entry is most significant word address

## Slide 10: Review: Memory Organization
• Bytes are nice, but most data items use larger "words"
• For MIPS, a word is 32 bits or 4 bytes.
Registers hold 32 bits of data
232 bytes with byte addresses from 0 to 232-1
• 230 words with byte addresses 0, 4, 8, ... 232-4
• Words are aligned
i.e., what are the least 2 significant bits of a word address?
Notes: All positive numbers - no sign bit
last entry is most significant byte address
fourth from last entry is most significant word address

## Slide 11: Aside: Beyond Numbers
American Std Code for Info Interchange (ASCII): 8-bit bytes representing characters
ASCII | Char |  | ASCII | Char | ASCII | Char | ASCII | Char |  | ASCII | Char | ASCII | Char
0 | Null |  | 32 | space | 48 | 0 | 64 | @ |  | 96 | ` | 112 | p
1 |  |  | 33 | ! | 49 | 1 | 65 | A |  | 97 | a | 113 | q
2 |  |  | 34 | “ | 50 | 2 | 66 | B |  | 98 | b | 114 | r
3 |  |  | 35 | # | 51 | 3 | 67 | C |  | 99 | c | 115 | s
4 | EOT |  | 36 | $ | 52 | 4 | 68 | D |  | 100 | d | 116 | t
5 |  |  | 37 | % | 53 | 5 | 69 | E |  | 101 | e | 117 | u
6 | ACK |  | 38 | & | 54 | 6 | 70 | F |  | 102 | f | 118 | v
7 |  |  | 39 | ‘ | 55 | 7 | 71 | G |  | 103 | g | 119 | w
8 | bksp |  | 40 | ( | 56 | 8 | 72 | H |  | 104 | h | 120 | x
9 | tab |  | 41 | ) | 57 | 9 | 73 | I |  | 105 | i | 121 | y
10 | LF |  | 42 | * | 58 | : | 74 | J |  | 106 | j | 122 | z
11 |  |  | 43 | + | 59 | ; | 75 | K |  | 107 | k | 123 | {
12 | FF |  | 44 | , | 60 | < | 76 | L |  | 108 | l | 124 | ¦
15 |  |  | 47 | / | 63 | ? | 79 | O |  | 111 | o | 127 | DEL
Notes: see Figure 3.15 in the book for the complete listing - note that we are only using 7 of the 8 bits (7 bits gives us 127 encodings) - the extra bit can be used as a parity bit to detect single bit errors during transmission
Note that upper and lower case letters differ by exactly 32
13 is carriage return
0 is Null (marking the end of string in C)

## Slide 12: MIPS Arithmetic Instructions
MIPS assembly language arithmetic statement
add $t0, $s1, $s2
sub $t0, $s1, $s2
Each arithmetic instruction performs only one operation
Each arithmetic instruction fits in 32 bits and specifies exactly three operands
  destination  source1 op source2
Those operands are all contained in the datapath’s register file ($t0,$s1,$s2) – indicated by $
Operand order is fixed (destination first)
Notes: For class handout

## Slide 13: MIPS Arithmetic Instructions
MIPS assembly language arithmetic statement
add $t0, $s1, $s2
sub $t0, $s1, $s2
Each arithmetic instruction performs only one operation
Each arithmetic instruction fits in 32 bits and specifies exactly three operands
  destination  source1 op source2
Each arithmetic instruction performs only one operation
Each arithmetic instruction fits in 32 bits and specifies exactly three operands
  destination  source1 op source2
Operand order is fixed (destination first)
Those operands are all contained in the datapath’s register file ($t0,$s1,$s2) – indicated by $
In Hexadecimal: 012A4020
000000
01001
01010
01000
00000
100000
Binary:
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
Fieldsize:
Notes: For lecture

## Slide 14
Example 1
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Store
Next
Instruction
Fetch next inst from memory:012A4020
opcode
rs
rt
rd
funct
shamt
Decode fields to get : ADD $8 $9 $10
“Retrieve” register values: $9 $10
Add $9 to $10
Place this sum in $8
Prepare to fetch instruction that follows the ADD in the program.
Syntax: ADD $8 $9 $10
Semantics: $8 = $9 + $10
Notes: For lecture

## Slide 15: Aside: MIPS Register Convention
Name | Register Number | Usage | Preserve on call?
$zero | 0 | constant 0 (hardware) | n.a.
$at | 1 | reserved for assembler | n.a.
$v0 - $v1 | 2-3 | returned values | no
$a0 - $a3 | 4-7 | arguments | yes
$t0 - $t7 | 8-15 | temporaries | no
$s0 - $s7 | 16-23 | saved values | yes
$t8 - $t9 | 24-25 | temporaries | no
$gp | 28 | global pointer | yes
$sp | 29 | stack pointer | yes
$fp | 30 | frame pointer | yes
$ra | 31 | return addr (hardware) | yes

## Slide 16: MIPS Register File
Register File
src1 addr
src2 addr
dst addr
write data
32 bits
src1
data
src2
data
32
locations
32
5
32
5
5
32
Holds thirty-two 32-bit registers
  Two read ports and
  One write port
Registers are
  Faster than main memory
    But register files with more locations are slower (e.g., a 64 word file could be as much as 50% slower than a 32 word file)
    Read/write port increase impacts speed quadratically
  Easier for a compiler to use
    e.g., (A*B) – (C*D) – (E*F) can do multiplies in any order vs. stack
  Can hold variables so that
    code density improves (since register are named with fewer bits than a memory location)
write control
Notes: All machines (since 1975) have used general purpose registers
How many bits wide are each of the lines going into/out of the register file?

## Slide 17: Machine Language - Add Instruction
Instructions, like registers and words of data, are 32 bits long
Arithmetic Instruction Format (R format):
add $t0, $s1, $s2
op rs rt rd shamt funct
op 6-bits opcode that specifies the operation
rs 5-bits register file address of the first source operand
rt 5-bits register file address of the second source operand
rd 5-bits register file address of the result’s destination
shamt 5-bits shift amount (for shift instructions)
funct 6-bits function code augmenting the opcode

## Slide 18: MIPS Memory Access Instructions
MIPS has two basic data transfer instructions for accessing memory
lw $t0, 4($s3) #load word from memory
sw $t0, 8($s3) #store word to memory
The data is loaded into (lw) or stored from (sw) a register in the register file – a 5 bit address
The memory address – a 32 bit address – is formed by adding the contents of the base address register to the offset value
  A 16-bit field meaning access is limited to memory locations within a region of 213 or 8,192 words (215 or 32,768 bytes) of the address in the base register
  Note that the offset can be positive or negative
Notes: What is the memory address of the given load and store instructions if $s3 contains the address 24?

## Slide 19: Machine Language - Load Instruction
Load/Store Instruction Format (I format):
lw $t0, 24($s2)
op rs rt 16 bit offset
Memory
data
word address (hex)
0x00000000
0x00000004
0x00000008
0x0000000c
0xf f f f f f f f
$s2
0x12004094
2410 + $s2 =
. . . 0001 1000
+ . . . 1001 0100
. . . 1010 1100 =
0x120040ac
0x120040ac
$t0
Notes: destination address no longer in the rd field - now in the rt field
offset limited to 16 bits - so can’t get to every location in memory (with a fixed base address)

## Slide 20: Example 2
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Store
Next
Instruction
Fetch the load inst from memory
“Retrieve” register value: $2
Compute memory address: 32 + $2
Load memory address contents into: $1
Prepare to fetch instr that follows the LW in the program. Depending on load semantics, new $1 is visible to that instr, or not until the following instr (”delayed loads”).
Decode fields to get : LW $1, 32($2)
opcode
rs
rt
offset
“I-Format”
Notes: What is the memory address of the given load and store instructions if $s3 contains the address 24?

## Slide 21: Machine Language - Load Instruction
Load/Store Instruction Format (I format):
Notes: destination address no longer in the rd field - now in the rt field
offset limited to 16 bits - so can’t get to every location in memory (with a fixed base address)

## Slide 22: Byte Addresses
Since 8-bit bytes are so useful, most architectures address individual bytes in memory
  The memory address of a word must be a multiple of 4 (alignment restriction)
Big Endian: leftmost byte is word address
    IBM 360/370, Motorola 68k, MIPS, Sparc, HP PA
Little Endian: rightmost byte is word address
    Intel 80x86, DEC Vax, DEC Alpha (Windows NT)
msb
lsb
3 2 1 0
little endian byte 0
0 1 2 3
big endian byte 0
Notes: Talk about the reasons (performance) for the word/byte alignment restriction

## Slide 23: Aside: Loading and Storing Bytes
MIPS provides special instructions to move bytes
lb $t0, 1($s3) #load byte from memory
sb $t0, 6($s3) #store byte to memory
op rs rt 16 bit offset
What 8 bits get loaded and stored?
  load byte places the byte from memory in the rightmost 8 bits of the destination register
    what happens to the other bits in the register?
  store byte takes the byte from the rightmost 8 bits of a register and writes it to a byte in memory
    what happens to the other bits in the memory word?
Notes:   load byte takes the contents of the byte at the memory address specified, zero-extends it, and loads it into the register
  It leaves the other bits in the memory word intact.

## Slide 24: MIPS Control Flow Instructions
MIPS conditional branch instructions:
bne $s0, $s1, Lbl #go to Lbl if $s0$s1 beq $s0, $s1, Lbl #go to Lbl if $s0=$s1
  Ex: if (i==j) h = i + j;
bne $s0, $s1, Lbl1 add $s3, $s0, $s1 Lbl1: ...
Instruction Format (I format):
op rs rt 16 bit offset
How is the branch destination address specified?

## Slide 25: Specifying Branch Destinations
Use a register (like in lw and sw) added to the 16-bit offset
  which register? Instruction Address Register (the PC)
    its use is automatically implied by instruction
    PC gets updated (PC+4) during the fetch cycle so that it holds the address of the next instruction
  limits the branch distance to -215 to +215-1 instructions from the (instruction after the) branch instruction, but most branches are local anyway
PC
Add
32
32
32
32
32
offset
16
32
00
sign-extend
from the low order 16 bits of the branch instruction
branch dst
address
?
Add
4
Notes: Note that two low order 0’s are concatenated to the 16 bit field giving an eighteen bit address
0111111111111111 00 = 2**15 –1 words (2**17 – 1 bytes)

## Slide 26: Example 4 Branch Instructions: BEQ $1,$2,25
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Store
Next
Instruction
Fetch branch inst from memory
“Retrieve” register values: $1, $2
Compute if we take branch: $1 == $2 ?
Decode fields to get: BEQ $1, $2, 25
opcode
rs
rt
offset
“I-Format”
ALWAYS prepare to fetch instr that follows the BEQ in the program (”delayed branch”). IF we take branch, the instr we fetch AFTER that instruction is PC + 4 + 100.
PC == “Program Counter”
Notes: Note that two low order 0’s are concatenated to the 16 bit field giving an eighteen bit address
0111111111111111 00 = 2**15 –1 words (2**17 – 1 bytes)

## Slide 27: The Program Counter (I)
Notes: Note that two low order 0’s are concatenated to the 16 bit field giving an eighteen bit address
0111111111111111 00 = 2**15 –1 words (2**17 – 1 bytes)

## Slide 28: The Program Counter (II)
Notes: Note that two low order 0’s are concatenated to the 16 bit field giving an eighteen bit address
0111111111111111 00 = 2**15 –1 words (2**17 – 1 bytes)

## Slide 29: The Program Counter (III)
Notes: Note that two low order 0’s are concatenated to the 16 bit field giving an eighteen bit address
0111111111111111 00 = 2**15 –1 words (2**17 – 1 bytes)

## Slide 30: More Branch Instructions
We have beq, bne, but what about other kinds of brances (e.g., branch-if-less-than)? For this, we need yet another instruction, slt
Set on less than instruction:
slt $t0, $s0, $s1 # if $s0 < $s1 then # $t0 = 1 else # $t0 = 0
Instruction format (R format):
op rs rt rd funct

## Slide 31: More Branch Instructions, Con’t
Can use slt, beq, bne, and the fixed value of 0 in register $zero to create other conditions
  less than blt $s1, $s2, Label
  less than or equal to ble $s1, $s2, Label
  greater than bgt $s1, $s2, Label
  great than or equal to bge $s1, $s2, Label
slt $at, $s1, $s2 #$at set to 1 if
bne $at, $zero, Label # $s1 < $s2
Such branches are included in the instruction set as pseudo instructions - recognized (and expanded) by the assembler
  Its why the assembler needs a reserved register ($at)
For more visit http://en.wikibooks.org/wiki/ MIPS_Assembly/Pseudoinstructions
Notes: For lecture
blt $s1,$s2 Label =
slt $at,$s1,$s2 #at gets 1 if $s1 < $s2
bne $at,$zero,Label

## Slide 32: Other Control Flow Instructions
MIPS also has an unconditional branch instruction or jump instruction: j label #go to label
Instruction Format (J Format):
op 26-bit address
PC
4
32
26
32
00
from the low order 26 bits of the jump instruction
Notes: If-then-else code compilation

## Slide 33: Aside: Branching Far Away
What if the branch destination is further away than can be captured in 16 bits?
The assembler comes to the rescue – it inserts an unconditional jump to the branch target and inverts the condition
beq $s0, $s1, L1
becomes
bne $s0, $s1, L2
j L1
L2:

## Slide 34: Instructions for Accessing Procedures
MIPS procedure call instruction: jal ProcedureAddress #jump and link
Saves PC+4 in register $ra to have a link to the next instruction for the procedure return
Machine format (J format):
Then can do procedure return with a
jr $ra #return
Instruction format (R format):
op 26 bit address
op rs funct
Notes: jr jumps to the address stored in the register – in this case $ra – which is just what we want.

## Slide 35: Instructions for Accessing Procedures
Notes: jr jumps to the address stored in the register – in this case $ra – which is just what we want.

## Slide 36: Instructions for Accessing Procedures
Notes: jr jumps to the address stored in the register – in this case $ra – which is just what we want.

## Slide 37: Aside: Spilling Registers
What if the callee needs more registers? What if the procedure is recursive?
  uses a stack – a last-in-first-out queue – in memory for passing additional values or saving (recursive) return address(es)
One of the general registers, $sp, is used to address the stack (which “grows” from high address to low address)
  add data onto the stack – push
    $sp = $sp – 4 data on stack at new $sp
  remove data from the stack – pop
    data from stack at $sp $sp = $sp + 4
low addr
high addr
$sp
top of stack
Notes: Note that temporary registers $t0 through $t9 can also be used as by MIPS convention they are not preserved by the callee (kept intact) across subroutine boundaries
However, saved registers $s0 through $s7 must be preserved by the calle - I.e., if the callee uses one, it must first save it and then restore it to its old value before returning control to the caller

## Slide 38: MIPS Immediate Instructions
addi $sp, $sp, 4 #$sp = $sp + 4
slti $t0, $s2, 15 #$t0 = 1 if $s2<15
Machine format (I format):
op rs rt 16 bit immediate
I format
Small constants are used often in typical code
Possible approaches?
  put “typical constants” in memory and load them
  create hard-wired registers (like $zero) for constants like 1
  have special instructions that contain constants !
The constant is kept inside the instruction itself!
  Immediate format limits values to the range +215–1 to -215
Notes: in gcc 52% of arithmetic operations involve constants – in spice its 69%
have the students answer why not – speed and limited number of registers
much faster than if loaded from memory
addi and slti do sign extend of immediate operand into the leftmost bits of the destination register (ie., copies the leftmost bit of the 16-bit immediate value into the upper 16 bits)
by contrast, ori and andi loads zero’s into the upper 16 bits and so is usually used (instead of the addi) to build 32 bit constants

## Slide 39: Aside: How About Larger Constants?
We'd also like to be able to load a 32 bit constant into a register, for this we must use two instructions
a new "load upper immediate" instruction
lui $t0, 1010101010101010
Then must get the lower order bits right, use ori $t0, $t0, 1010101010101010
1010101010101010
0000000000000000
1010101010101010
0000000000000000
1010101010101010 1010101010101010
16 0 8 1010101010101010
Notes: For lecture
sets the upper 16 bits of a constant in a register, allowing the next instruction to specify the lower 16 bits of the constant
note that lui fills the lower 16 bits of the register with zero’s
why can’t addi be used as the second instruction for this 32 bit constant?
also note – the assembler lets me specify constants larger than 16 bits in one instruction and then expands the code into two instructions (lui and ori) automatically

## Slide 40: Example
x[10]=x[11]+c
Assume c corresponds to register $t0 and array x has a base address of 4,000,000 10

## Slide 41: Example

## Slide 42: Example

## Slide 43: MIPS Organization So Far
Processor
Memory
32 bits
230
words
read/write
addr
read data
write data
word address
(binary)
0…0000
0…0100
0…1000
0…1100
1…1100
Register File
src1 addr
src2 addr
dst addr
write data
32 bits
src1
data
src2
data
32
registers
($zero - $ra)
32
32
32
32
32
32
5
5
5
PC
ALU
32
32
32
32
32
0
1
2
3
7
6
5
4
byte address
(big Endian)
Fetch
PC = PC+4
Decode
Exec
Add
32
32
4
Add
32
32
branch offset

## Slide 44: MIPS ISA So Far
Category | Instr | Op Code | Example | Meaning
Arithmetic (R & I format) | add | 0 and 32 | add $s1, $s2, $s3 | $s1 = $s2 + $s3
 | subtract | 0 and 34 | sub $s1, $s2, $s3 | $s1 = $s2 - $s3
 | add immediate | 8 | addi $s1, $s2, 6 | $s1 = $s2 + 6
 | or immediate | 13 | ori $s1, $s2, 6 | $s1 = $s2 v 6
Data Transfer (I format) | load word | 35 | lw $s1, 24($s2) | $s1 = Memory($s2+24)
 | store word | 43 | sw $s1, 24($s2) | Memory($s2+24) = $s1
 | load byte | 32 | lb $s1, 25($s2) | $s1 = Memory($s2+25)
 | store byte | 40 | sb $s1, 25($s2) | Memory($s2+25) = $s1
 | load upper imm | 15 | lui $s1, 6 | $s1 = 6 * 216
Cond. Branch (I & R format) | br on equal | 4 | beq $s1, $s2, L | if ($s1==$s2) go to L
 | br on not equal | 5 | bne $s1, $s2, L | if ($s1 !=$s2) go to L
 | set on less than | 0 and 42 | slt $s1, $s2, $s3 | if ($s2<$s3) $s1=1 else $s1=0
 | set on less than immediate | 10 | slti $s1, $s2, 6 | if ($s2<6) $s1=1 else $s1=0
Uncond. Jump (J & R format) | jump | 2 | j 2500 | go to 10000
 | jump register | 0 and 8 | jr $t1 | go to $t1
 | jump and link | 3 | jal 2500 | go to 10000; $ra=PC+4
Notes: similarity of the binary representation of related instructions simplifies the hardware design

## Slide 45: Review of MIPS Operand Addressing Modes
Register addressing – operand is in a register
Base (displacement) addressing – operand is at the memory location whose address is the sum of a register and a 16-bit constant contained within the instruction
  Register relative (indirect) with 0($a0)
  Pseudo-direct with addr($zero)
Immediate addressing – operand is a 16-bit constant contained within the instruction
op rs rt rd funct
Register
word operand
base register
op rs rt offset
Memory
word or byte operand
op rs rt operand

## Slide 46: Review of MIPS Instruction Addressing Modes
PC-relative addressing –instruction address is the sum of the PC and a 16-bit constant contained within the instruction
Pseudo-direct addressing – instruction address is the 26-bit constant contained within the instruction concatenated with the upper 4 bits of the PC
op rs rt offset
Program Counter (PC)
Memory
branch destination instruction
op jump address
Program Counter (PC)
Memory
jump destination instruction
||

## Slide 47: MIPS (RISC) Design Principles
Simplicity favors regularity
  fixed size instructions – 32-bits
  small number of instruction formats
  opcode always the first 6 bits
Good design demands good compromises
  three instruction formats
Smaller is faster
  limited instruction set
  limited number of registers in register file
  limited number of addressing modes
Make the common case fast
  arithmetic operands from the register file (load-store machine)
  allow instructions to contain immediate operands

## Slide 48: Next Lecture and Reminders
Next lecture
  MIPS ALU Review
    Reading assignment – PH, Chapter 3
Too much to Handle