## Slide 1: CSE 340 Computer Architecture Spring 2018 MIPS Arithmetic Review
Notes: Other handouts
HW#1
To handout next time

## Slide 2: Review: MIPS Organization
Processor
Memory
32 bits
230
words
read/write
addr
read data
write data
word address
(binary)
0…0000
0…0100
0…1000
0…1100
1…1100
Register File
src1 addr
src2 addr
dst addr
write data
32 bits
src1
data
src2
data
32
registers
($zero - $ra)
32
32
32
32
32
32
5
5
5
PC
ALU
32
32
32
32
32
0
1
2
3
7
6
5
4
byte address
(big Endian)
Fetch
PC = PC+4
Decode
Exec
Add
32
32
4
Add
32
32
branch offset

## Slide 3: Review: MIPS Addressing Modes
1. Operand: Register addressing
op rs rt rd funct
Register
word operand
The simplest addressing mode is the register addressing. Instructions using registers execute fast because they do not have the delay associated with memory access. But, the number of registers is limited since only 5-bits are reserved to select a register. Register addressing is a form of direct addressing. The value in the register is an operand instead of being a memory address to an operand.

## Slide 4: Review: MIPS Addressing Modes
op rs rt offset
2. Operand: Base addressing
base register
Memory
word or byte operand
In base register addressing we add a small constant to a pointer held in a register. The register may point to a structure or some other collection of data, and we need to load a value at a constant offset from the beginning of the structure. Because each MIPS instruction fits in one word, the size of the constant is limited to 16 bits.

## Slide 5: Review: MIPS Addressing Modes
3. Operand: Immediate addressing
op rs rt operand
MIPS immediate addressing means that one operand is a constant within the instruction itself. The advantage of using it is that there is no need to have extra memory access to fetch the operand. But keep in mind that the operand is limited to 16 bits in size.
The jump instruction format can also be considered as an example of immediate addressing, since the destination is held in the instruction.

## Slide 6: Review: MIPS Addressing Modes
4. Instruction: PC-relative addressing
op rs rt offset
Program Counter (PC)
Memory
branch destination instruction
PC-relative addressing is used for conditional branches. The address is the sum of the program counter and a constant in the instruction. Here is an example to help you understand it.
Beqz = Branch to address/location if the variable = 0

## Slide 7: Review: MIPS Addressing Modes
5. Instruction: Pseudo-direct addressing
op jump address
Program Counter (PC)
Memory
jump destination instruction
||

## Slide 8: MIPS Number Representations
32-bit signed numbers (2’s complement): 0000 0000 0000 0000 0000 0000 0000 0000two = 0ten 0000 0000 0000 0000 0000 0000 0000 0001two = + 1ten ...
0111 1111 1111 1111 1111 1111 1111 1110two = + 2,147,483,646ten 0111 1111 1111 1111 1111 1111 1111 1111two = + 2,147,483,647ten 1000 0000 0000 0000 0000 0000 0000 0000two = – 2,147,483,648ten 1000 0000 0000 0000 0000 0000 0000 0001two = – 2,147,483,647ten ...
1111 1111 1111 1111 1111 1111 1111 1110two = – 2ten 1111 1111 1111 1111 1111 1111 1111 1111two = – 1ten
maxint
minint
Converting <32-bit values into 32-bit values
  copy the most significant bit (the sign bit) into the “empty” bits 0010 -> 0000 0010 1010 -> 1111 1010
  sign extend versus zero extend (lb vs. lbu)
MSB
LSB

## Slide 9: MIPS Arithmetic Logic Unit (ALU)
Must support the Arithmetic/Logic operations of the ISA
  add, addi, addiu, addu
  sub, subu, neg
  mult, multu, div, divu
  sqrt
  and, andi, nor, or, ori,
  xor, xori
  beq, bne, slt, slti, sltiu, sltu
32
32
32
m (operation)
result
A
B
ALU
4
zero
ovf
1
1
With special handling for
  sign extend – addi, addiu andi, ori, xori, slti, sltiu
  zero extend – lbu, addiu, sltiu
  no overflow detected – addu, addiu, subu, multu, divu, sltiu, sltu

## Slide 10: Review: 2’s Complement Binary Representation
2’sc binary | decimal
1000 | -8
1001 | -7
1010 | -6
1011 | -5
1100 | -4
1101 | -3
1110 | -2
1111 | -1
0000 | 0
0001 | 1
0010 | 2
0011 | 3
0100 | 4
0101 | 5
0110 | 6
0111 | 7
23 - 1 =
-(23 - 1) =
-23 =
1010
complement all the bits
1011
and add a 1
Negate
Notes: Signed numbers – assuming 2’s complement representation – for eight bits
Note that msb of 1 indicates a negative number, the bit string all 0’s is zero, that the largest positive number that can be represented is 7 (2**(n-1) –1 for n bits) whereas the largest negative number that can be represented is –8 (-2**(n-1) for n bits)

## Slide 11: Overflow Detection
Overflow: the result is too large to represent in 32 bits
Overflow occurs when
  adding two positives yields a negative
  or, adding two negatives gives a positive
  or, subtract a negative from a positive gives a negative
  or, subtract a positive from a negative gives a positive
On your own: Prove you can detect overflow by:
  Carry into MSB xor Carry out of MSB, ex for 4 bit signed numbers
0
1
1
1
0
0
1
1
+
7
3
1
1
0
0
1
0
1
1
+
–4
– 5
Notes: For class handout

## Slide 12: Overflow Detection
Overflow: the result is too large to represent in 32 bits
Overflow occurs when
  adding two positives yields a negative
  or, adding two negatives gives a positive
  or, subtract a negative from a positive gives a negative
  or, subtract a positive from a negative gives a positive
On your own: Prove you can detect overflow by:
  Carry into MSB xor Carry out of MSB, ex for 4 bit signed numbers
1
1
1
1
0
1
0
1
1
0
0
1
1
1
0
0
1
1
+
7
3
0
1
– 6
1
1
0
0
1
0
1
1
+
–4
– 5
7
1
0
Notes: For lecture
Recalled from some earlier slides that the biggest positive number you can represent using 4-bit is 7 and the smallest negative you can represent is negative 8.
So any time your addition results in a number bigger than 7 or less than negative 8, you have an overflow.
Keep in mind is that whenever you try to add two numbers together that have different signs, that is adding a negative number to a positive number, overflow can NOT occur.
Overflow occurs when you to add two positive numbers together and the sum has a negative sign. Or, when you try to add negative numbers together and the sum has a positive sign.
If you spend some time, you can convince yourself that If the Carry into the most significant bit is NOT the same as the Carry coming out of the MSB, you have a overflow.

## Slide 13: Tailoring the ALU to the MIPS ISA
Need to support the logic operation (and,nor,or,xor)
  Bit wise operations (no carry operation involved)
  Need a logic gate for each function, mux to choose the output
Need to support the set-on-less-than instruction (slt)
  Use subtraction to determine if (a – b) < 0 (implies a < b)
  Copy the sign bit into the low order bit of the result, set remaining result bits to 0
Need to support test for equality (bne, beq)
  Again use subtraction: (a - b) = 0 implies a = b
  Additional logic to “nor” all result bits together
Immediates are sign extended outside the ALU with wiring (i.e., no logic needed)

## Slide 14: Shift Operations
Also need operations to pack and unpack 8-bit characters into 32-bit words
Shifts move all the bits in a word left or right
sll $t2, $s0, 8 #$t2 = $s0 << 8 bits
srl $t2, $s0, 8 #$t2 = $s0 >> 8 bits
op rs rt rd shamt funct
Notice that a 5-bit shamt field is enough to shift a 32-bit value 25 – 1 or 31 bit positions
Such shifts are logical because they fill with zeros
Notes: also have sllv, srlv, and srav

## Slide 15: Shift Operations, con’t
An arithmetic shift (sra) maintain the arithmetic correctness of the shifted value (i.e., a number shifted right one bit should be ½ of its original value; a number shifted left should be 2 times its original value)
  so sra uses the most significant bit (sign bit) as the bit shifted in
  sra $t2, $s0, 8 #$t2 = $s0 >> 8 bits
The shift operation is implemented by hardware separate from the ALU
  using a barrel shifter (which would takes lots of gates in discrete logic, but is pretty easy to implement in VLSI)

## Slide 16: Multiply
Binary multiplication is just a bunch of right shifts and adds
multiplicand
multiplier
partial
product
array
double precision product
n
2n
n
can be formed in parallel and added in parallel for faster multiplication

## Slide 17: MIPS Multiply Instruction
Multiply produces a double precision product
mult $s0, $s1 # hi||lo = $s0 * $s1
  Low-order word of the product is left in processor register lo and the high-order word is left in register hi
  Instructions mfhi rd and mflo rd are provided to move the product to (user accessible) registers in the register file
op rs rt rd shamt funct
Multiplies are done by fast, dedicated hardware and are much more complex (and slower) than adders
Hardware dividers are even more complex and even slower;
Notes: multu – does multiply unsigned
Both multiplies ignore overflow, so its up to the software to check to see if the product is too big to fit into 32 bits. There is no overflow if hi is 0 for multu or the replicated sign of lo for mult.

## Slide 18: Division
Division is just a brunch of quotient digit guesses and left shifts and subtracts
dividend
divisor
partial
remainder
array
quotient
n
n
remainder
n
0
0
0
0
0
0

## Slide 19: MIPS Divide Instruction
Divide generates the reminder in hi and the quotient in lo
div $s0, $s1 # lo = $s0 / $s1
# hi = $s0 mod $s1
  Instructions mfhi rd and mflo rd are provided to move the quotient and reminder to (user accessible) registers in the register file
As with multiply, divide ignores overflow so software must determine if the quotient is too large. Software must also check the divisor to avoid division by 0.
op rs rt rd shamt funct
Notes: Seems odd to me that the machine doesn’t support a double precision dividend in hi || lo but it looks like it doesn’t

## Slide 20: Representing Big (and Small) Numbers
What if we want to encode the approx. age of the earth?
  4,600,000,000 or 4.6 x 109
or the weight in kg of one a.m.u. (atomic mass unit)
  0.0000000000000000000000000166 or 1.6 x 10-27
There is no way we can encode either of the above in a 32-bit integer.
Floating point representation (-1)sign x F x 2E
  Still have to fit everything in 32 bits (single precision)
s E (exponent) F (fraction)
1 bit 8 bits 23 bits
  The base (2, not 10) is hardwired in the design of the FPALU
  More bits in the fraction (F) or the exponent (E) is a trade-off between precision (accuracy of the number) and range (size of the number)
Notes: Notice that in scientific notation the mantissa is represented in normalized form (no leading zeros)

## Slide 21: IEEE 754 FP Standard Encoding
Most (all?) computers these days conform to the IEEE 754 floating point standard (-1)sign x (1+F) x 2E-bias
  Formats for both single and double precision
  F is stored in normalized form where the msb in the fraction is 1 (so there is no need to store it!) – called the hidden bit
  To simplify sorting FP numbers, E comes before F in the word and E is represented in excess (biased) notation
Single Precision |  | Double Precision |  | Object Represented
E (8) | F (23) | E (11) | F (52) | 
0 | 0 | 0 | 0 | true zero (0)
0 | nonzero | 0 | nonzero | ± denormalized number
± 1-254 | anything | ± 1-2046 | anything | ± floating point number
± 255 | 0 | ± 2047 | 0 | ± infinity
255 | nonzero | 2047 | nonzero | not a number (NaN)
Notes: Book distinguishes between the representation with the hidden bit there – significand (the 24 bit version) , and the one with the hidden bit removed – fraction (the 23 bit version)

## Slide 22: Floating Point Addition
Addition (and subtraction)
(F1  2E1) + (F2  2E2) = F3  2E3
  Step 1: Restore the hidden bit in F1 and in F2
  Step 1: Align fractions by right shifting F2 by E1 - E2 positions (assuming E1  E2) keeping track of (three of) the bits shifted out in a round bit, a guard bit, and a sticky bit
  Step 2: Add the resulting F2 to F1 to form F3
  Step 3: Normalize F3 (so it is in the form 1.XXXXX …)
    If F1 and F2 have the same sign  F3 [1,4)  1 bit right shift F3 and increment E3
    If F1 and F2 have different signs  F3 may require many left shifts each time decrementing E3
  Step 4: Round F3 and possibly normalize F3 again
  Step 5: Rehide the most significant bit of F3 before storing the result
Notes: Note that smaller significand is the one shifted (while increasing its exponent until its equal to the larger exponent)
overflow/underflow can occur during addition and during normalization
rounding may lead to overflow/underflow as well

## Slide 23: MIPS Floating Point Instructions
MIPS has a separate Floating Point Register File ($f0, $f1, …, $f31) (whose registers are used in pairs for double precision values) with special instructions to load to and store from them
lwcl $f1,54($s2) #$f1 = Memory[$s2+54]
swcl $f1,58($s4) #Memory[$s4+58] = $f1
And supports IEEE 754 single
add.s $f2,$f4,$f6 #$f2 = $f4 + $f6
and double precision operations
add.d $f2,$f4,$f6 #$f2||$f3 = $f4||$f5 + $f6||$f7
similarly for sub.s, sub.d, mul.s, mul.d, div.s, div.d

## Slide 24: MIPS Floating Point Instructions, Con’t
And floating point single precision comparison operations
c.x.s $f2,$f4 #if($f2 < $f4) cond=1; else cond=0
where x may be eq, neq, lt, le, gt, ge
and branch operations
bclt 25 #if(cond==1) go to PC+4+25
bclf 25 #if(cond==0) go to PC+4+25
And double precision comparison operations
c.x.d $f2,$f4 #$f2||$f3 < $f4||$f5 cond=1; else cond=0

## Slide 25: Next Lecture and Reminders
Next lecture
  Addressing and understanding performance
    Reading assignment – PH, Chapter 4